Final Project

Course	IT 32O, WAN Technology and Application

Instructor	John Green

Given the following narrative description, user information and printouts, draw a network diagram of the configuration. Include all ports, addresses, subnet masks, DCE/DTE and connection type. Indicate the method of routing each router is using.

The SellMore Company is establishing its presence over the country. They have purchased stores and facilities in three US cities and have a headquarters in Dallas, Texas. The company will wholesale their goods to local merchants from New York, Jacksonville, San Jose and their headquarters. They own part of the 152.10.x.x class B subnet, from 152.10.0.0 through 152.10.8.255

Director of Network Ops:

- I want to maintain our network structure within our allocated IP ranges.

- Each sales location needs to have the ability to handle 40 computers.

- The Headquarters needs to handle 80 computers.

- We have enough money for one router at each location, no more.

- We can buy additional ports per router; you will have to work with that.

Network Admin, HQ - Your boss

- Don't get fancy with your naming schemes; routers should identify themselves by location.

- Identify the stub networks for the sales teams at each location so I don't confuse them with the subnets used for routing.

- Draw you diagram clearly so we can understand it, remember someone else is going to have to implement it.

- Do yourself a favor and use the right connections where you need to. The last guy kept drawing 100BaseTx to different cities. You know what happened to him.

- Don't mess with the two running networks we have up in Dallas, The HQ building is running on 152.10.0.0/24 and the sales facility is on 152.10.1.0/24. The boss will not look kindly if we, I mean you, mess that up.

- Oh yea, that last guy set up two of the routers. I think he did it correctly since he was an ITT graduate.

NEWYORK

service timestamps debug uptime

service timestamps log uptime

service password-encryption

!

hostname newyork

!

enable secret password

!

ip host newyork 152.10.4.2 152.10.5.1 152.10.8.1

ip host dallas 152.10.0.1 152.10.1.1 152.10.2.1 152.10.3.1 152.10.4.1

ip host jacksonville 152.10.3.2 152.10.5.2 152.10.6.1

ip host sanjose 152.10.2.2 152.10.7.1

!

ip subnet-zero

!

interface FastEthernet0/0

ip address 152.10.8.1 255.255.255.0

no ip directed-broadcast

duplex auto

speed auto

no shutdown

!

interface Serial0/0

ip address 152.10.4.2 255.255.255.0

no ip directed-broadcast

no ip mroute-cache

no fair-queue

clockrate 64000

no shutdown

!

interface Serial0/1

ip address 152.10.5.1 255.255.255.0

no ip directed-broadcast

clockrate 64000

no shutdown

!

router rip

network 152.10.0.0

!

ip classless

no ip http server

no ip domain-lookup

!

!

line con 0

transport input none

password password

login

!

line aux 0

!

line vty 0 4

password password

login

!

no scheduler allocate

end

----------------------------------------

SANJOSE

service timestamps debug uptime

service timestamps log uptime

service password-encryption

!

hostname sanjose

!

enable secret password

!

ip host newyork 152.10.4.2 152.10.5.1 152.10.8.1

ip host dallas 152.10.0.1 152.10.1.1 152.10.2.1 152.10.3.1 152.10.4.1

ip host jacksonville 152.10.3.2 152.10.5.2 152.10.6.1

ip host sanjose 152.10.2.2 152.10.7.1

!

ip subnet-zero

!

interface FastEthernet0/0

ip address 152.10.7.1 255.255.255.0

duplex auto

speed auto

no shutdown

!

interface Serial0/0

no ip address

no ip directed-broadcast

no ip mroute-cache

shutdown

no fair-queue

!

interface Serial0/1

ip address 152.10.2.2 255.255.255.0

no ip directed-broadcast

no shutdown

!

router rip

network 152.10.0.0

!

ip classless

no ip http server

no ip domain-lookup

!

line con 0

transport input none

password password

login

!

line aux 0

!

line vty 0 4

password password

login

!

no scheduler allocate

end

--------------------------------